## Slide 1
Base

## Slide 2
Add Motherboard
Sits on the base’s shelf

## Slide 3
Add Motherboard
Sits on the base’s shelf
Attached with a single screw
Using Belleville washer

## Slide 4
Add Motherboard
Sits on the base’s shelf
Attached with a single screw
Using Belleville washer

## Slide 5
Add Thermal Straps
Between the base and 2 unused holes on the Motherboard
Possibly add these for the other 3 unused holes as well

## Slide 6
Add Lid
Covers the half of the Motherboard that carries the Carrier/Mezzanine boards
Outlet for the air pump out port

## Slide 7
Add Lid
Covers the half of the Motherboard that carries the Carrier/Mezzanine boards
Attached to the base in 3 spots
Untapped holes through the lid and tapped on the base

## Slide 8
Add Lid
Covers the half of the Motherboard that carries the Carrier/Mezzanine boards
Attached to the base in 3 spots
Untapped holes through the lid and tapped on the base

## Slide 9
Connect to Dewar
4 screws, 1 in each corner
Untapped holes through lid and base
Dewar 4K plate has tapped holes
Screws are 5x10”

## Slide 10
Connect to Dewar
4 screws, 1 in each corner
Untapped holes through lid and base
Dewar 4K plate has tapped holes
Screws are 5x10”

## Slide 11
Cutout
Outlet for the air pump out port
Meander for escaping air during pump down and limiting radon passage during transport
Tapped holes for connecting thermal straps

## Slide 12
Questions:
How much clearance do we need above the board?
Do we know exactly how thick the PCB will be?
How much clearance do we need below the board?